PTN Electronics

VGA Matrix Switchers System

User Manual

Please read this manual carefully before using this product.

Notice：

Contents

1. Introduction	4

1.1  About MVG Matrix Switcher System	4

1.2  MVG Matrix Switcher Models	4

2. Packing of the Product	5

3. Installation	5

4. Front View of the Product	6

4.1  Front View of the MVG44A	6

4.2  Front View of the MVG82A、MVG84A、MVG88A	6

4.3  Front View of the MVG164A、MVG168A、MVG1616A	6

5. Rear View of the Product	7

5.1  Rear View of the VGA44A	7

5.2  Rear View of the WVG8	7

5.3  Rear View of the WVG16、WVG32	7

5.4  Rear View of the MVG82A、MVG84A、MVG88A	7

5.5  Rear View of the MVG164A、MVG168A、MVG1616A	8

6. External Connection	8

6.1  Introduction of the Input and Output Connectors	8

6.2  Connection of RS-232 Communication Port	8

6.2.1  Connection with Control Systems	9

6.2.2  Connection with Computer	9

6.3  How to Connect with the Input and Output Terminals	9

6.4  How to Connect with the MVG I/O Devices	11

7. Operation of the Control Panel	11

7.1  Front Panel Description	11

7.2  Command Format of the Switching Operation	11

7.3  Examples of Operation	12

8. Usage of the Remote Controller	13

9. Communication Protocol and Command Codes	14

10. Technical Specifications	16

11. Troubleshooting & Maintenance	18

# 1. Introduction

## 1.1 About MVG Matrix Switcher System

MVG series Matrix switcher is a high-performance professional computer and audio signal switcher that can be used for cross switching of multi computer and audio signal.

MVG series switcher mostly apply in broadcasting TV engineering, multi-media meeting room, big screen display engineering, television education, command control center or other fields. It provides power-fail locale protection function, LED indicating, shortcut selecting function. With RS232 interface, it can be worked with PC, remote control system and any other far-end control system devices . The user manual takes MVG88 as the example; other models can take reference from it too.

F 1-1 MVG 88A

## 1.2 MVG Matrix Switcher Models

According to different situation and users, the MVG series can be classified into the following models:

| Specifications Models | Video Inputs | Video Outputs | RS232 Interface | Audio I/O |
| --- | --- | --- | --- | --- |
| MATRIX WVG8A | 8 | 1 | √ | × |
| MATRIX WVG16A | 16 | 1 | √ | × |
| MATRIX WVG32A | 32 | 1 | √ | × |
| MATRIX MVG44A | 4 | 4 | √ | √ |
| MATRIX MVG82 | 8 | 2 | √ | × |
| MATRIX MVG82A | 8 | 2 | √ | √ |
| MATRIX MVG84 | 8 | 4 | √ | × |
| MATRIX MVG84A | 8 | 4 | √ | √ |
| MATRIX MVG88 | 8 | 8 | √ | × |
| MATRIX MVG88A | 8 | 8 | √ | √ |
| MATRIX MVG164 | 16 | 4 | √ | × |
| MATRIX MVG164A | 16 | 4 | √ | √ |
| MATRIX MVG168 | 16 | 8 | √ | × |
| MATRIX MVG168A | 16 | 8 | √ | √ |

# 2. Packing of the Product

MVG Matrix Host

RS-232 Communication Cord

Power Supply Cord

CD with Application

# 3. Installation

MVG matrix switchers adopt metal shell and can be stacked with other device. Moreover, they are rack-mountable enclosure and can be installed in the standard 19” rack.

F 3-1 Installing the MVG matrix switcher in the standard 19” rack

# 4. Front View of the Product

## 4.1 Front View of the MVG44A

F 4-1 Front view of the MVG44A

## 4.2  Front View of the MVG82A、MVG84A、MVG88A

F 4-4 Front view of the MVG82A、MVG84A、MVG88A

## 4.3  Front View of the MVG164A、MVG168A、MVG1616A

F 4-5 Front view of the MVG164A、MVG168A、MVG1616A

# 5. Rear View of the Product

## 5.1  Rear View of the VGA44A

F 5-1  Rear view of the VGA44A

## 5.2 Rear View of the WVG8

F 5-2  Rear view of the WVG8

## 5.3 Rear View of the WVG16、WVG32

F 5-3  Rear view of the WVG16,WVG32

## 5.4 Rear View of the MVG82A、MVG84A、MVG88A

F 5-4  Rear view of the MVG82A、MVG84A、MVG88A

## 5.5 Rear View of the MVG164A、MVG168A、MVG1616A

F 5-5  Rear view of the MVG164A、MVG168A 、MVG1616A

# 6. External Connection

## 6.1 Introduction of the Input and Output Connectors

The MVG matrix switchers adopt female 15-pin HD connectors as the video signal I/O interface, and captive screw connectors as the audio signal I/O interface. Please refer to the rear view figure of the model concerned for details.

## 6.2 Connection of RS-232 Communication Port

Except the front control panel, infrared remote controller (Optional) and the Ethernet control (Optional), the MVG matrix switcher can be controlled from far-end control systems via the RS-232 communication port.

This RS-232 communication port is a female 9-pin D connector. The definition of its pins is as the table below.

Pin     　　　 RS-232　　　 Description

- N/u          Not used

- Tx           Transmit data

- Rx           Receive data

- N/u          Not used

- Gnd          Signal ground

- N/u          Not used

- N/u          Not used

- N/u          Not used

- N/u          Not used

### 6.2.1 Connection with Control Systems

With the RS-232 port, can control and communicate with the switcher remotely.

### 6.2.2 Connection with Computer

When the switcher connects to the COM1 or COM2 of the computer with control software, users can control it by that computer.

To control the switcher, users may use the RS232 software.

F 6-1  Connection between MVG matrix switcher and the computer

## 6.3 How to Connect with the Input and Output Terminals

The MVG matrix switchers may take laptops, desktop computers, graphic workstations and document cameras as their input signal source, and projectors, RP TVs, displayers and amplifiers as their output signal destinations.

VGA Connection:

The MVG matrix switchers support all kinds of the RGB and VGA signal sources with 15-PIN HD VGA connectors.

The 15-PIN HD VGA connector is shown as the figure below.

| Pin | RGB | YcbCr |
| --- | --- | --- |
| 1 | R | Cr |
| 2 | G | Y |
| 3 | B | Cb |
| 4 | Not used |  |
| 5 | Ground |  |
| 6 | R ground | Cr ground |
| 7 | G ground | Y ground |
| 8 | B ground | Cb ground |
| 9 | Not used |  |
| 10 | Sync signal ground |  |
| 11 | Not used |  |
| 12 | Not used |  |
| 13 | H or H/V |  |
| 14 | V |  |
| 15 | Not used |  |

F 6-2   15-PIN HD VGA connector

If the RGB device doesn’t with VGA output terminals, please convert the signals with an RGB to VGA switcher for getting high quality VGA output effects.

Please use the special VGA signal cord to connect the input and output devices and connect the 15-Pin HD connectors carefully.

Audio Signal Connection:

Audio connection is little complicated than video. It has two kinds of connection: balanced and unbalanced.

The balanced connection transmits a pair of balanced signals with two signal cords. Because interferences will have the same intensity and the opposite phases on the two signal cords, it will be counteracted in the end. For the low frequency extent of the audio signal, it would be easily interfered under long distance transmission. Therefore，as an anti-interference connection , it is mostly used in audio connection of special device.

The unbalanced connection transmits signals only with a signal cord. Without counteraction, it can be interfered more easily. Accordingly, it is adopted for household appliance or some cases with low technical demand.

The two kinds of connection are shown below.

F 6-3  Balanced/unbalanced connection on captive screw connector

The connection should be selected is up to the interface of the device. When available, the balanced connection is the first choice. Before connection, please read the command or relevant demand in the user manual carefully. In some cases, maybe there is balanced in source signal end but unbalanced in the destination end. If in a nonstandard case, it is done to connect balanced for the balanced end and unbalanced for unbalanced end. But if in a standard one, the converter must be used to switch the signals as the same, balanced or unbalanced.

F 6-4  Connection of MVG matrix switcher system

## 6.4 How to Connect with the MVG I/O Devices

VGA/VGA signal converter is for the VGA signal source without VGA output ports, such as: desktop computers and notebooks. It can convert the VGA signals to VGA signals.

F 6-5	Connection of VGA I/O devices

# 7. Operation of the Control Panel

## 7.1 Front Panel Description

“AV”         AV synchronal button: To transfer video and audio signal synchronously by the switcher

Example: To transfer both the video and the audio signals from input channel No.3 to output channel No.4.

Operation: Press buttons in this order “AV”,“3”,, “4””.

“VIDEO”      Video button: To transfer only video signals from input channel to output channel

Example: To transfer video signals from input channel No.3 to output channel No.4.

Operation: Press buttons in this order “VIDEO”, “3”, “4”.

“AUDIO”     Audio button: To transfer only audio signals from input channel to output channel

Example: To transfer audio signals from input channel No.2 to output channel No.3.

Operation: Press buttons in this order ““AUDIO”, “2”, “3””.

“1,2,3,4”  	I/O Keypads: Keys to select I/O channels.

Example: To transfer input channel No.3 to output channel No.1

Operation: Press buttons in this order : “3” in INPUT area, “1” in OUTPUT area.

## 7.2 Command Format of the Switching Operation

With the front control panel, the switcher could be control directly and rapidly by pressing the buttons under below format.

“Menu” +“Input Channel” +“Output Channel 1”

“Menu”:  “AV”, “Audio”, “Video”

“Input Channel”: Fill with the number of input channel to be controlled

“Output Channel”: Fill with the number of output channels to be controlled

## 7.3 Examples of Operation

Example 1：To transfer video and audio signals from input channel No.1 to output channel No.3,4

1, Press the button for switching mode “AV” for the switching mode of video and audio (“Audio” for the switching mode of audio only; “Video” for the switching mode of video only)

2, Press the button for input channel number“1”

3,Press the button for the first output channel number “3”

4, Press the button for the second output channel number “4”

Then, switching OK !  audio/video switching from “1” to “3” and “4”

# 8. Usage of the Remote Controller

With the infrared remote controller, the matrix switcher could be control remotely. Because the function buttons on the remote controller are the same with the ones on the front control panel, the remote controller shares the same control operation and command format with the control panel.

# 9. Communication Protocol and Command Codes

With this command system, the RS232 software is able to control and operate the MCV Matrix remotely.

Communication protocol:

Baud rate: 9600         Data bit: 8         Stop bit: 1         Parity bit: none

| Command Types | Command Codes | Functions |
| --- | --- | --- |
| System Command | /*Type; | Inquire the models information. |
|  | /%Lock; | Lock the keyboard of the control panel on the Matrix. |
|  | /%Unlock; | Unlock the keyboard of the control panel on the Matrix. |
|  | /^Version; | Inquire the version of firmware |
|  | /:MessageOff; | Turn off the feedback command from the com port. It will only show the “switcher OK”. |
|  | /:MessageOn; | Turn on the feedback command from the com port. |
|  | Undo. | To cancel the previous operation. |
|  | Demo. | Switch to the “demo” mode, 1->1, 2->2, 3->3 … and so on. |
|  | [x1]All. | Transfer signals from the input channel [x1] to all output channels |
|  | All#. | Transfer all input signals to the corresponding output channels respectively. |
|  | All$. | Switch off all the output channels. |
|  | [x1]#. | Transfer signals from the input channel [x1] to the output channel [x1]. |
|  | [x1]$. | Switch off the output channel [x1]. |
| Operation Command （PTN2.0 Command System） | [x1] V[x2]. | Transfer the video signals from the input channel [x1] to the output channel [x2]. |
|  | [x1] V[x2],[x3],[x4]. | Transfer the video signals from the input channel [x1] to the output channels [x2], [x3] and [x4]. |
|  | [x1] A[x2]. | Transfer the audio signals from the input channel [x1] to the output channel [x2]. |
|  | [x1] A[x2],[x3],[x4]. | Transfer the audio signals from the input channel [x1] to the output channels [x2], [x3] and [x4]. |
|  | [x1] B[x2]. | Transfer both the video and the audio signals from the input channel [x1] to the output channel [x2]. |
|  | [x1] B[x2],[x3],[x4]. | Transfer both the video and the audio signals from the input channel [x1] to the output channels [x2], [x3] and [x4]. |
|  | Status[x1]. | Inquire the input channel to the output channel [x1]. |
|  | Status. | Inquire the input channel to the output channels one by one. |
|  | Save[Y]. | Save the present operation to the preset command [Y]. [Y] ranges from 0 to 9. |
|  | Recall[Y]. | Recall the preset command [Y]. |
|  | Clear[Y]. | Clear the preset command [Y]. |

Note:

1. [x1], [x2], [x3] and [x4] are the symbols of input or output channels ranged according to the model of the matrix switcher. If the symbols exceed the effective range, it would be taken as a wrong command.

2. In above commands, “[”and “]” are symbols for easy reading and do not need to be typed in actual operation.

3. Please remember to end the commands with the ending symbols “.” and “;”.

Detail Examples:

- Transfer signals from an input channel to all output channels: [x1]All.

Example: To transfer signals from the input channel No.3 to all output channels.  Run Command: “3All.”

- Transfer all input signals to the corresponding output channels respectively: All#.

Example: If this command is carried out on an MVG1616-A matrix switcher, the status of it will be: 1->1, 2->2, 3->3, 4->4……16->16.

- Switch off all the output channels: All$.

Example: After running this command, there will be no signals on all the output channels.

- Check the version of the firmware: /^Version;

To check the version of the firmware.

- Switch off the detail feedback command from the COM port: /:MessageOff;

Switch off the detail feedback information from the COM port. But, it will leave the “switch OK” as the feedback, when you switch the matrix.

- Switch on the detail feedback command from the COM port: /:MessageOn;

Switch on the detail feedback information from the COM port. it will show the detail switch information when it switch. Example: when switch 1->2 for Audio, it will feedback “A0102”.

- Transfer signals from an input channel to the corresponding output channel: [x]#.

Example: To transfer signals from the input channel No.5 to the output channel No.5.  Run Command: “5#.”

8、Switch off an output channel: [x]$.

Example: To switch off the output channel No.5.  Run Command: “5$.”

9、Switch video signals command: [x1] V[x2].

Example: To transfer the video signals from the input channel No.3 to the output channel No.5.

Run Command: “3V5.”

10、Switch audio signals command: [x1] A[x2].

Example: To Transfer the audio signals from the input channel No.10 to the output channel

Run Command: “10A2.”

11、Switch both video and audio signals synchronously: [x1] B[x2].

Example: To transfer both the video and the audio signals from the input channel No.120 to the output channel No.12,13,15.  Run Command: “120B12,13,15.”

12、Inquire the input channel to the output channel [x]: Status[x].

Example: To inquire the input channel to the output channel No.23.  Run Command: “Status23.”

13、Inquire the input channel to the output channels one by one: Status.

Example: To inquire the input channel to the output channels one by one.  Run Command: “Status.”

14、Save the present operation to the preset command [Y]: Save[Y].

Example: To save the present operation to the preset command No.7.  Run Command: “Save7.”

15、Recall the preset command [Y]: Recall[Y].

Example: To recall the preset command No.5.  Run Command: “Recall5.”

16、Clear the preset command [Y]: Clear[Y].

Example: To clear the preset command No.5.  Run Command: “Clear5.”

# 10. Technical Specifications

| Series Specifications | MVG44A | MVG8 series | MVG16 series | WVG8 | WVG32 series |
| --- | --- | --- | --- | --- | --- |
| Video |  |
| Models included | MVG44A | MVG82A MVG84A MVG88A | MVG164A MVG168A | WVG8 | WVG32 WVG 64 WVG 96 |
| Gain | 0 dB |
| Bandwidth | 250MHz (-3dB), fully loaded |
| Cross talk sum | -60dB @10 MHz， -39dB @100 MHz |
| Switching speed | 200 ns (Max) |
| Signal type | VGA，VGAS， RGsB， RsGsBs， HDTV， Component video，S-video， Composite video |
| Input video |  |
| Connector | Female 15-pin HD |
| Signal strength | 1V p-p Y component video、S-video，composite video； 0.7V p-p VGA；0.3V p-p R-Y & B-Y component video、 S-video |
| Maximum/Minimum level | Analog signals: 0.5V ~ 2.0V p-p |
| Impedance | 75 Ω |
| Echo loss | <-40dB@5MHz |
| Horizontal frequency response | 15 kHz ~ 145 kHz |
| Vertical frequency response | 30 Hz ~ 170 Hz |
| Max error in DC offset | 15mV |
| Output video |  |
| Connector | Female 15-pin HD |
| Maximum/Minimum level | 2.0V p-p |
| Impedance | 75 Ω |
| Echo loss | <-40dB@5MHz |
| Max compensation in Dc offset | ±5mV |
| Sync signal |  |
| Input/output signals | RGBHV, RGBS, RGsB, RsGsBs, Component video， Composite video |
| Video system | NTSC 3.58，NTSC 4.43，PAL，SECAM |
| Input level | 0.5V- 5.0V p-p,: 4.0V p-p normal |
| Output level | AGC-TTL: 5Vp-p, unterminated |
| Input impedance | 510 Ω |
| Output impedance | 75 Ω |
| Maximum transmission delay | Horizontal:90ns Vertical:160ns |
| Maximum ascending/ descending time | 4ns |
| Polarity | Straight or subtractive according to input |
| Audio signal |  |
| I/O connector | 3.8mm with screw , 5 pole |
| Gain | 0dB |
| Frequency respond | 20 Hz ~ 20 kHz, |
| General harmonic distortion + noise | 0.05% @ 1 kHz （under rating voltage） |
| S/N | >90dB |
| Segregation rate | >80dB @ 1 kHz |
| CMRR | >75dB @: 20 Hz ~ 20 kHz |
| Signal | Stereo ，balanced /unbalanced |
| Impedance | Input：>10 kΩ（balanced /unbalanced） Output：50 Ω （unbalanced）, 100 Ω（balanced） |
| Maximum input level | +19.5dBu, （balanced /unbalanced） |
| Gain error | ±0.1dB @20 Hz ~ 20 kHz |
| Max output level | +19.5dBu, （balanced /unbalanced） |
| Control type |  |
| Serial control port | RS-232, 9-pin FD connector |
| Baud rate and protocol | Baud rate: 9600 Data bit: 8 Stop bit: 1 Parity bit: none |
| Serial control poling protocol | 2 = TX, 3 = RX, 5 = GND |
| Control application | Switch 2.0 |
| Features |  |
| Power supply | 100VAC ~ 240VAC, 50/60 Hz, universal international power supply |
| Temperature | Storing and operating temperature: -20° ~ +70°C |
| Humidity | Storing and operating humidity: 10% ~ 90% |
| Size | 485(L)X245(W)X445mm(H) | 485(L)X260(W)X90mm(H) | 485(L)X260(W)X140mm(H) | 485(L)X245(W)X445mm(H) | 485(L)X260(W)X90mm(H) |
| weight | 1.8kg | 3.5kg | 4.3kg | 1.8kg | 3.5kg |
| MTBF | 30,000 hours |
| Quality guarantee | 1 year free guarantee |

# 11. Troubleshooting & Maintenance

- When the output image in the destination device connected to the MVG Matrix has ghost, such as the projector output with ghost, please check the projector’s setting or try another high quality connection cord.

- When there is a color losing or no video signal output, it may be the unmatched VGA connector order between the input and output end.

- When the remote controller doesn’t works:

  - Maybe the battery is run out of, please change a new one.

  - Maybe the controller is broken, please ask the dealer to fix it.

- When user can not control the MVG Matrix by computer through its COM port, please check the COM port number in the software and make sure the COM port is in good condition.

- When switching , the beeper beeps but without any output image：

  - Check with oscilloscope or multimeter if there is any signal at the input end. If there is no signal input, it may be the input connection cord broken or the connectors loosen.

  - Check with oscilloscope or multimeter if there is any signal at the output end. If there is no signal output, it may be the output connection cord broken or the connectors loosen.

  - Please make sure the destination device is exactly on the controlled output channel

  - If it is still the same after the above checking, it may be something wrong in the switcher. Please send it to the dealer for fixing.

- If the output image is interfered, please make sure the system is earthed well.

- If the static becomes stronger when connecting the BNC connectors, it may be due to the incorrect earthing of the power supply, Please earth it again correctly, and otherwise it would bring damage to the switcher or shorten its natural life.

- If the Matrix can not be controlled by the keys on the front panel, RS232 port or remote controller, the host may has already been broken. Please send it to the dealer for fixing.

# Text boxes

Menu, for switching source and function

This MVG Matrix Switchers User Manual takes example of the Matrix model MVG88A. It can be used as user’s manual of other MVG matrix switcher models.

This manual is only an instruction for operators, not for any maintenance usage. The functions described in this version are updated till Jan 2010. Any changes of functions and parameters since then will be informed separately. Please refer to the dealers for the latest details.

This manual is copyright PTN Electronics Limited. All rights reserved. No part of this publication may be copied or reproduced without the prior written consent of PTN Electronics Limited.

All product function is valid till 2010-1-1

The inputs channels, from 0~9, and plusing “10+” for more

MVG Series ---Computer Graphics (VGA)/Stereo Audio Matrix Switcher

In order to ensure the credibility use of the product and the user’s safety, please comply with the following items during installation and maintenance:

The system must be earthed properly. Please do not use two blades plugs and ensure the alternating power supply ranged from 100v to 240v and from 50Hz to 60Hz.

Do not put the switcher in a place of too hot or too cold.

To avoid any damage by over heat, please keep the working environment good in ventilation to radiate the heat when running the switcher.

The switchers should be turned off when in rainy and humid days or nonuse for a long time,

The alternating power supply line should be disconnected with the power socket during the following operation.

  - Take out or reinstall any component of the switcher

  - Disconnect or re-connect any connector of the switcher

Please do not attempt to maintain and uncover the switcher for there is a high-voltage component inside and the risk of the electric shock.

Do not splash any chemical product or liquid on or near the equipment.

The outputs channels, from 0~9, and plusing “10+” for more

The inputs channels, from 0~9, and plusing “10+” for more

Safety Operation Guide